## Slide 1
HKN ECE 411 Midterm 1 Review Session
Keshav Harisrikanth, Eric Roch, Saransh Sinha

## Slide 2
Instruction Set Architecture (ISA)
Performance, Energy, Power
Memory Hierarchy
Caches
Virtual Memory (VM)
Pipelines and Hazards
MPs
Agenda

## Slide 3
5 Basic types of ISA:
  Accumulator
  Stack
  Mem-Mem
  Reg-Mem
  Load-Store
Instruction Set Architecture
Other design considerations:
  Fixed vs variable instr. length, register count, number of opcodes
Tradeoffs?

## Slide 4
Be able to:
  Convert between any ISAs
  Evaluate performance
    HW and SW
  Consider new ISAs
Larger ISA Categories
  RISC vs. CISC
  REG vs MEM
ISA (cont.)
stack | accumulator | register (register-memory) | register (load-store)
push A push B add pop C | load A add B store C | load R1, A add R1, B store C, R1 | load R1,A load R2, B add R3, R1, R2 store C, R3

## Slide 5
Single-cycle vs Multi-cycle tradeoffs…
= Relative frequency (fraction) of instructions of type
Performance

## Slide 6
Amdahl's Law
  parallelizable fraction (code), number of processing units
Classic Dennard Scaling and the End
Energy & Power

## Slide 7
Locality (Temporal vs Spatial)
  Temporal: Reference same memory location multiple times at short intervals
  Spatial: Reference neighboring memory addresses
Average Memory Access Time (AMAT)
Memory Hierarchy

## Slide 8
Types of Caches
  Direct Mapped
    Memory Value can be placed at a single corresponding location in cache
    Fast Indexing mechanism
Caches

## Slide 9
Types of Caches
  Set Associative (Two way in image)
    Memory Value can be placed into a set of locations in cache
    More complex mechanism
Caches

## Slide 10
Types of Caches
  Fully Associative
    Memory Value can be placed into any location in cache
    Very complex mechanism
    required to search cache
    such as CAM
Caches

## Slide 11
Three C’s
  Compulsory Misses: Cold start misses (no valid data at start)
  Capacity Misses: Cache is full, and needs to evict
  Conflict Misses: Wrong tag at index, cache may not be full
Replacement Policies
  Least Recently Used (LRU, pLRU)
  Not Most Recently Used (Not-MRU)
  Least Frequently Used (LFU)
Cache Characteristics

## Slide 12
Num bits VPN ≥ PPN
More addressable space than physical memory
Homonym Problem:
  1 Virtual Address maps to multiple Physical Addresses
Synonym Problem:
  Multiple Virtual Addresses map to 1 Physical Address
Virtual Memory

## Slide 13
Num bits VPN ≥ PPN
More addressable space than physical memory
Homonym Problem:
  1 Virtual Address maps to multiple Physical Addresses
Synonym Problem:
  Multiple Virtual Addresses map to 1 Physical Address
Virtual Memory
Homonym Solution:
  Flush TLB and caches on context switch
Synonym Solution:
  Depends on cache size and page size

## Slide 14
Virtually-Indexed, Virtually-Tagged (VIVT)
  Very fast access time
  Susceptible to homonym and synonym problem
VIVT Cache

## Slide 15
Physically-Indexed, Physically-Tagged (PIPT)
  Slower access time
  Not susceptible to homonym and synonym problem
  Simpler coherence
PIPT Cache

## Slide 16
Virtually-Indexed, Physically-Tagged (VIPT)
  Very fast access time (Parallelize TLB and Cache)
  Not susceptible to homonym
    Synonym problem remains under certain conditions
VIPT Cache

## Slide 17
Page Table Walk
Be prepared for 391-esque page table/entry sizing.
Be able to break down address as used.
Flat vs n-Level
  2 Level for x86
Address Translation

## Slide 18
What can be pipelined?
Why does pipelining improve performance?
What extra considerations do pipelines add?
  Hazards (and their various solutions)
The “Classic” 5 Stage RISC Pipeline:
Pipelining

## Slide 19
Structural – Limitation
on functional units.
Data – Same data has different values at different stages.
Control – Control flow of the program is incorrect.
  Branch prediction.
Hazards

## Slide 20
SystemVerilog Proficiency
  Tasks, Functions
  Procedural Statements
  Be able to trace a waveform with SV.
Verification fundamentals
  Stressing input stimuli
  Error reporting
MPs: MP0

## Slide 21
RISC-V
Memory structures
  Alignment
Multicycle processors
For more, take ECE 385
MPs: MP1

## Slide 22
Questions?