## Slide 1: ECE 120 Midterm 3
Keshav Harisrikanth
Joseph Ravichandran, Srijan Chakraborty, Kanad Sarkar

## Slide 2: Topic Overview
Finite State Machine
  Analysis, Design, Counter Design
Memory
  Flip flops, RAM, Tri-state buffer
  Addressability
  How to construct from smaller blocks
LC3
  Von Neumann Architecture
  LC3 Architecture
  ISA
  Instruction Cycle

## Slide 3: S'-R' Latch
If S = R, then Q and P can't store a bit.
When S' is 0 and R' is 1, stores 1 into Q.
When S' is 1 and R' is 0, stores 0 into Q.

## Slide 4: D latch
D stands for the DATA, WE stands for Write Enable
Stores the value of D when WE is high.

## Slide 5: D Flip Flops
Made from two D latches
D latch behavior:
D flip flop stores the input bit D when clock goes low to high
C | D | R | S | Q+ | Definition
1 | 0 | 1 | 0 | 0 | Reset
1 | 1 | 0 | 1 | 1 | Set
0 | 0 | 0 | 0 | Q | No change
0 | 1 | 0 | 1 | 1 | No change

## Slide 6: Bit Slice Design
Design 1 component for a single bit
Repeat it k times for a k-bit design
Example of bit slice design: Ripple Carry Adder

## Slide 7: Serialized Design
Same as a bit slice design, except instead of many bit slices only use 1
Use flip-flops to store intermediate results
Compute each bit slice in sequence, over time

## Slide 8: Serialized Design
The ‘F’ Signal is 1 when the first bit of data enters, 0 otherwise
Use the ‘F’ signal to initialize your registers to the correct value
  In the full adder example, this means load the register with carry in of 0

## Slide 9: Bit Slice VS Serial
Area
  For large number of bits, serial uses less area
  For smaller number of bits, bit slice uses less area
Speed
  Bit slice is usually faster
  Serial is usually slower

## Slide 10: Tri-State Buffers
When enable is 1, they act as a wire
When enable is 0, they act as high impedance (disconnected)

## Slide 11: Finite State Machine
3 Main Components of FSMs:
Next state logic
Current state
Output logic
How many bits are needed to represent N states in a standard FSM?

## Slide 12: FSMs In Detail
2 types: Mealy and Moore
  Moore: Outputs are a function of current state only
  Mealy: Outputs are a function of current state and inputs
  Mealy machines use less states
5 key elements:
  Finite number of states
  Finite number of inputs
  Finite number of outputs
  Explicit number of state transitions
  Explicit definition of outputs as a function of state (and as function of inputs for Mealy machines)

## Slide 13: FSM Design
List all inputs to your FSM
List all outputs from the FSM
Create a truth table for the FSM
  State and inputs on the left
  Next state and outputs on the right
  Outputs should be the same for the same current state (unless Mealy machine)
Create a state diagram
K-maps, etc.

## Slide 16
EVERY 16 BIT INSTRUCTION CORRESPONDS TO ONE OF THESE!
CHEAT SHEET IS YOUR SAVIOR HERE!
Side: Don't worry about JSR, JSRR, TRAP, or RTI yet, just know they exist

## Slide 17: How to read your Cheat Sheet (for ISA)

## Slide 18: Instruction Cycle!

## Slide 19: Details
FETCH
  MAR ← PC
  PC ← PC+1
  MDR ← M[MAR]
  IR ← MDR
  Used to obtain the next instruction
  IMPORTANT! PC is incremented to next spot BEFORE current instruction put in IR
DECODE
- Opcode (IR[15:12]) examined (first 4 bits)