## Slide 1: ECE 120 Midterm 2
HKN Review Session

## Slide 2: Overview of Review
CMOS logic, Boolean expressions, Boolean Algebra
K-maps, SOP, POS
2-level networks
Adders, ALUs, and Bit Slice Design
Multiplexers, Decoders
Flip-Flops and Latches (S-R & D)
FSM Design, Moore Machines
Practice Exams! (The not so secret sauce in success)

## Slide 3: CMOS logic
Metal Oxide Semiconductor Field Effect Transistors (MOSFET)
  N-type: pull-down, voltage applied (1) means it conducts, voltage absent (0) means it is off
  P-type: pull-up, voltage applied (1) means it is off, voltage absent (0) means it is on
Complementary layout
  Prevents floating / short-circuited outputs
  Requires p-type on top (connected to Vdd), requires that the top is the dual of the bottom
NAND Gate

## Slide 4: Boolean Expressions and Algebra
 | * indicates AND | + indicates OR
identity | 1 * A = A | 0 + A = A
null | 1 + A = 1 | 0 * A = 0
idempotence | A + A = A | A * A = A
complementarity | A * A’ = 0 | A + A’ = 1
DEMORGAN | (A + B)’ = A’B’ | (AB)’ = A’ + B’
involution | (x’)’ = x | 
Distribution | (A + B)C = AC + BC | AB + C = (A + C)(B + C)
Consensus | (A + B)(A’ + C)(B + C) = (A + B)(A’ + C) | AB + A’C + BC = AB + A’C

## Slide 5: Duality Principle, Ex. Demorgan’s Law
Duality: swap 1’s and 0’s, swap AND’s and OR’s, maintain precedence using parentheses
Complement: find dual, complement each variable
m(a,b,c,d) = a’ + bc’ + b’d’
Dual: n(a,b,c,d) = a’(b+c’)(b’+d’)
m(a,b,c,d) = ((a’ + bc’ + b’d’)’)’
m(a,b,c,d) = (a(bc’)’(b’d’)’)’

## Slide 6: Logical Equivalence
2 ways to prove that two boolean functions are equivalent
Use truth tables: if they have the same output over all input combinations then they are logically equivalent
Use boolean algebra properties to show equality.
Let’s prove deMorgan’s law:
(A + B)’: So, we can see in this truth table that (A+B)’ is logically equivalent to A’B’. QED.
A | B | (A+B)’ | A’B’
0 | 0 | 1 | 1
0 | 1 | 0 | 0
1 | 0 | 0 | 0
1 | 1 | 0 | 0

## Slide 7: Logical Completeness
A set of gates is said to be logically complete if it can implement any boolean expression with exclusively those set of gates.
For example, NAND and NOR are individually logically complete as well as AND, OR, and NOT together.
  How?
  What about NOT? Is NOT logically complete?
  What about XOR?

## Slide 8: K(arnaugh)-maps
A way to represent the outputs of a logical design with respect to its inputs
Should arrange inputs along row and columns in gray code order.
    00 01 11 10
Should be able to form whether asked to from a circuit, problem statement, or a design goal.
Can accommodate up to 4 inputs, more requires more than a 2d representation.
Simple example for a 3-input AND, f(A,B,C):
A, BC-> | 00 | 01 | 11 | 10
0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0

## Slide 9: SOP, POS
SOP- Sum of Products
  A group of products (ANDs) which are being summed (OR’d).
  Example: f(A,B) = AB’+A’B (XOR)
  AB’ and A’B are the products, which are summed.
POS- Product of Sums
  A group of sums (ORs) which are being multiplied (AND’d).
  Example: f(A,B) = (A+B)(A’+B’) (Still XOR)
  (A+B) and (A’+B’) are the sums, which are AND’d.

## Slide 10: Minimal vs. Canonical
Minimal - Listing terms as efficiently as possible (no redundancy)
  Can find through the bubbling method on kmaps.
  Example: f(A,B,C) = A+BC
Canonical - Listing every term of the function with every input.
  Can find through writing out a truth table.
  Canonical SOP: A listing of every set that makes the function return true (OR’d)
    Example for above f: f(A,B,C) = ABC+ABC’+AB’C+AB’C’+A’BC
  Canonical POS: A listing of every set that makes the function return false
    Example for above: f(A,B,C) = (A+B+C)(A+B+C’)(A+B’+C)
A | B | C | F
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1

## Slide 11: Converting SOP/POS to 2-level NAND or NOR
Any 2 level POS circuit can also be converted quickly to a NOR-NOR implementation.

## Slide 12: Optimized Boolean Expressions
When trying to find the Boolean expression for the outputs of an FSM
  consider both the POS and SOP forms
  Check which of these minimises the total number of gates
Prime implicants
  The largest grouping of 1’s not fully contained by another grouping of 1’s (with power of 2 dimensions, ie. 2,4,8)
Uniqueness
  Look for other prime implicants of equal size that are not currently being used in your minimal expression
  If you can write another function with the same number of terms, then it is not unique
Don’t Cares
  Symbol: X, used if the output can be a 0 or a 1
  Can be included in any kmap circling
  Important for making simplified SOP/POS (allows larger implicants)

## Slide 13: Latches (S-R & D)
This SR latch above is active High for S (set) and R (reset)
functionality. This SR latch is made from 8 transistors C is the enable bit for this D - Latch
This D - latch is made from 18 transistors

## Slide 14: How to build Flip-Flops from latches
Rising edge triggered flip flop on top, Falling edge triggered flip flop on the bottom.
Looking at the top picture we have a rising edge triggered flip flop. How?
When the clock is 0, master latch is write enabled, slave latch is write disabled. This way once the edge rises, the master latch becomes write disabled storing/holding the value of the input Dm from right before the rising edge. The WE of the slave (second) latch goes high allowing the value stored in the master to be written to and stored into the slave latch.

## Slide 15: Multiplexers and Decoders
Multiplexers:
n select bits
2n input options
1 output
Decoders:
1 enable bit
n select bits
(input lines specify which output to raise)
2n possible outputs (one high at a time)

## Slide 16: Multiplexers and Decoders
Implement g(a,b,c,d)=ab+a’b+ab’c+ab’c’d’ using a 4:1 MUX and no more than one extra gate.
A B
A/B/1
B/1
A/B/0
C
~D

## Slide 17: Adders and Bit Slice Design
Bit Slice Adder Circuit: broken down into repeated operations on individual bits, this design extends to any # of bits bc slices pass information between them

## Slide 18: ALUs
Combinational logic circuit that performs arithmetic & logic operations on integers

## Slide 19: FSMs (Probably Not on Test)
An FSM is composed of a set of states, (# of state bits = ceiling( log_2( # states ) ) )