## Slide 1: HKN ECE 310 Exam 2 Review Session
Corey Snyder

## Slide 2: Topics
DTFT and Frequency Response
Ideal Sampling and Reconstruction
DFT and FFT

## Slide 3: Discrete Time Fourier Transform
Important Properties:
  Periodicity by !
  Linearity
  Symmetries (Magnitude, angle, real part, imaginary part)
  Time shift and modulation
  Product of signals and convolution
  Parseval’s Relation

## Slide 4: Frequency Response
For any stable LSI system:
What is the physical interpretation of this?
  The DTFT is the z-transform evaluated along the unit circle!
Why is the frequency response nice to use in addition to the z-transform?
  is an eigenfunction of LSI systems
  By extension:

## Slide 5: Magnitude and Phase Response
Very similar to ECE 210
Frequency response, and all DTFTs for that matter, are periodic
Magnitude response is fairly straightforward
  Take the magnitude of the frequency response, remembering that = 1
For phase response:
  Phase is “contained” in terms
  Remember that cosine and sine introduce sign changes in the phase
    When a cosine or sine changes phase, we have a contribution of phase.
  Limit your domain from to .
For real-valued signals and systems:
  Magnitude response is even-symmetric
  Phase response is odd-symmetric

## Slide 6: DTFT Exercise 1
Let our signal be
Compute the DTFT of .
Plot the magnitude response.
Plot the phase response.

## Slide 7: DTFT Exercise 2
Suppose we have a new system defined by a real-valued impulse response with corresponding DTFT . We also know the following about the magnitude and phase responses:
Plot the magnitude response of on the interval to .
Plot the phase response of on the interval to .

## Slide 8: Sinusoidal Response Exercise 1
We have an LSI system defined by the following LCCDE:
Find .
Find .
Find the output to each of the following inputs:

## Slide 9: Ideal A/D Conversion
Sampling via an impulse train will yield infinitely many copies of the analog spectrum in the digital frequency domain
Important relations to recall:
Nyquist Sampling Theorem:
Relationship between digital and analog frequencies

## Slide 10: Ideal D/A Conversion
Recall that our DTFT has infinitely many copies of our sampled analog spectrum.
Ideal D/A conversion requires we perfectly recover only the central copy between and
  Digital signal is given notion of continuous-time back with a sampling period .
  We suppose that we have an ideal low-pass analog filter (“interpolation filter”) with cutoff frequency corresponding to .

## Slide 11: Sampling Exercise 1
Suppose we sampled some analog signal defined by
with sampling period to obtain the digital signal . Which of the following are possible values for ? (There may be more than one!)
rad/s
rad/s
rad/s
rad/s
rad/s

## Slide 12: Sampling Exercise 2
We have an analog signal with CTFT with maximum frequency .
For each of the following sampling periods , draw the sampled DTFT spectrum on the interval to .

## Slide 13: Discrete Fourier Transform
What is the relationship between the DTFT and the DFT?

## Slide 14: DFT Properties
Periodicity by
Circular shift
Circular modulation
Circular convolution
We must amend our DTFT properties with the “circular” term because the DFT is defined over a finite length signal and assumes periodic extension of that finite signal.

## Slide 15: Zero-Padding
We can improve the resolution of the DFT simply by adding zeros to the end of the signal.
This doesn’t change the frequency content of the DTFT!
  No information/energy is being added.
Instead, it increases the number of samples the DFT takes of the DTFT.
This can be used to improve spectral resolution.

## Slide 16: Windowing
Recall that the DFT implies infinite periodic extension of our signal.
This extension can lead to artifacts known as “spectral leakage”
Window functions help with these artifacts
  Rectangular window
  Hamming window
  Hanning window
  Kaiser window
Windowing is just multiplication in the time domain
We care about the main lobe width and side lobe attenuation of these windows.
  In particular, know the tradeoffs between the rectangular and Hamming windows

## Slide 17: Fast Fourier Transform
Class of “divide-and-conquer” algorithms to compute the DFT efficiently.
Naïve DFT takes operations, FFT takes .
Decimation in Time vs. Decimation in Frequency
Butterfly diagrams

## Slide 18: Fast Linear Convolution via FFT
Convolution in the time domain requires operations.
By convolution theorem, perhaps we can do better in the frequency domain?
Don’t forget multiplication in DFT domain is circular convolution in time.
To avoid aliasing, we adopt the following procedure
Given signal and filter of lengths and , respectively:
Zero-pad and to length
Take their FFTs
Multiply in frequency domain
Take the inverse FFT
This procedure takes operations.

## Slide 19: DFT Exercise 1
Surprisingly, we have another signal
For which value(s) of is the DFT of , , largest?
Suppose now that we zero-pad our sequence with 72 zeros to obtain . For which value(s) of is largest?